## Slide 1: 실험6 : Verilog Tutorial
논리 설계 및 실험
SNU VLSI LAB
Oct 26, 2022

## Slide 2
Verilog Introduction
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 3: What is Verilog
In the early days, integrated circuit engineers had to manually draw transistors and their connections on paper to design the integrated circuit
As circuits become larger and more complex, there was a need to have a better way of designing integrated circuits
HDL : Hardware Description Language
  The language that describes hardware functionality
  VHDL, Verilog
EX) Functionality of a up-down counter can be described easily

## Slide 4: What is Verilog
Converted to hardware schematic by software toolchain
Hardware schematic : diagram with logic gates and interconnection
Software toolchain converts Verilog code to netlist
  EX) Synopsys Design compiler, Xilinx Vivado
  Hardware schematic : visualization of netlist
Low development cost with HDL!

## Slide 5
Verilog Data Types
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 6: Verilog syntax
Comments : // or /* … */
Number Format
  Decimal, hexadecimal, binary, octal
  [size]’[base_format][number]

## Slide 7: Verilog syntax
Number Format
  Unsized
    ‘0 : all zeros
    ‘1 : all ones
  Negative
    Negative numbers are specified by placing a minus sign (-) before the size of a number
    2’b11 : decimal 3
    2’sb11 : decimal -1

## Slide 8: Verilog Date types
Data Types
  Net : EX) wire
  Variable : EX) reg
  Each bit position stores one of the four different values (0, 1, x, z)
  Wire : used to connect between hardware entities
  Reg : used to model hardware register or combinational logic
  Wire and reg have different ways to use

## Slide 9: Verilog scalar and vector
Scalar : 1bit
Vector : multi bit

## Slide 10: Verilog scalar and vector
Bit-selects
  Any bit in a vectored net or variable can be individually selected and assigned a new value
Part-selects
  A range of contiguous bits can be selected and assigned a new value

## Slide 11: Verilog array
Each element of array can be scalar or vector
Any number of dimensions can be created by specifying an address range after the identifier name
Left to right indexing

## Slide 12
Verilog Building Blocks
Module
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 13: Verilog module
Block of Verilog code that implements a certain functionality
The same module can be reused to form bigger modules that implement more complex hardware
EX) use dff module to form shift_reg module

## Slide 14: Verilog module
Module should be enclosed within module and endmodule keyword
Name of the module should be given right after the module keyword
Optional list of ports may be declared

## Slide 15: Verilog module
A module can contain multiple instances of other modules
A top level module is one which contains all other modules.
A top level module is not instantiated within any other module

## Slide 16: Verilog module
Port
  Set of signals that act as inputs and outputs to a particular module
  Direction : input, output, inout
  Default : wire

## Slide 17: Verilog module
<direction> [net_type] [signed] [range] <signal name>

## Slide 18: Verilog module
Module instantiations
  Modules can be instantiated within other modules and ports of these instances can be connected with other signals inside the parent module
  <module name> <instance name> (<port list>);
  Port connection by ordered list, Port connection by name
  Ports that are not connected to any wire will have a high-impedance value
  Ports of type Input or inout cannot be declared as reg

## Slide 19
Verilog Building Blocks
Statements
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 20: Verilog assign statement
Signals of type wire requires the continuous assignment of a value.
  When the circuit is running, the wire is continuously driven by some source
  This concept is realized by the assign statement where any wire can be driven continuously with a value. The value can either be a constant or an expression comprising of a group of signals
Assign statement rules
  LHS should always be wire type
  Whenever any operand on the RHS changes in value, LHS will be updated
Example #1 : AND gate
  Wire out is continuously driven by an expression of signals i1 & i2.

## Slide 21: Verilog assign statement
Example #1 : connection
Example #2 : AND gate
  Wire out is continuously driven by an expression of signals i1 & i2.
a
b

## Slide 22: Verilog assign statement
Example #3 : Combinational Logic
  and operation : &
  or operation : |
  xor operation : ^
  not operation : ~
Relative order of assign statements doesn’t matter.
  All assign statements are evaluated concurrently and continuously.

## Slide 23: Verilog Operators
https://class.ece.uw.edu/cadta/verilog/operators.html

## Slide 24: Verilog always statement
An always block is one of the procedural blocks. Statements inside an always block are executed sequentially
Sensitivity list
  Expression that defines when the always block should be executed.
  Specified after @ operator within parenthesis ()
LHS in always block must be reg type

## Slide 25: Verilog always statement
Blocking assignment
  The statements below the blocking assignment will be evaluated after the blocking assignment is evaluated
Non-blocking assignment
  The statements below the blocking assignment will be evaluated concurrently with the Non-blocking assignment
Just connection
Shift register

## Slide 26: Verilog always statement
Combinational logic with always statement
  Use only blocking statement
  Consider using “*” in sensitivity list (* means all signals on RHS)

## Slide 27: Verilog always statement
Sequential logic with always statement
  Use only Non-blocking statement
  @(negedge rstn) means async reset
Just connection
Shift register

## Slide 28
Verilog Behavioral modeling
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 29: Verilog Control blocks
Hardware behavior cannot be implemented without conditional statements and other ways to control the flow of logic
  multiplexer, decoder, etc…
Conditional statements
  If - else – if
  case
Iterative statements
  for

## Slide 30: Verilog Control blocks
Conditional statements
  If - else – if
If the expression evaluates to true, then the first statement will be executed. If false, else part will be executed.
If else must be used in always statement
else part is optional

## Slide 31: Verilog Control blocks
Conditional statements
  case
The case statement checks if the given expression matches one of the other expressions in the list and branches accordingly.
Matching is done in order (item1  itme2  item3  item4).
First matched item is executed.
If no item is matched, default statement is executed. But if there is no default statement, case statement is done without doing anything.

## Slide 32: Verilog Control blocks
Iterative statement
  For
for loop is to iterate a set of statements given within the loop as long as the given condition is true.
for loop is just unrolled when running module

## Slide 33: Verilog Parameters
Parameters are Verilog constructs that allow a module to be reused with a different specification.
  Adder with different bit width

## Slide 34
Verilog Simulation
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 35: Verilog Simulation Basics
Simulation
  Applying different input stimulus to the design at different times to check if the RTL code behaves the intended way.
Testbench
  module including a design module and testing it.

## Slide 36: Verilog Simulation Basics
Timescale
  `timescale directive specifies the time unit and precision
  <time_unit> : measurement of delays and simulation time
    #1 = 1ns delay when `timescale 1ns/<time_precision>
  <time_precision> : how delay values are rounded before used in simulation
    #1.4 = 1ns delay when `timescale 1ns/1ns
    #1.5 = 2ns delay when `timescale 1ns/1ns
    #1.1 = 1.1ns delay when `timescale 1ns/1ps

## Slide 37: Verilog Simulation Basics
initial statement
  Only for simulation. Not synthesizable
  initial block is started at the beginning of a simulation at time 0 unit.
  This block will be executed only once.
$finish : system task for finishing the simulation

## Slide 38
Verilog Appendix
Reference : https://www.chipverify.com/verilog/verilog-tutorial

## Slide 39: Verilog Operators
https://nandland.com/reduction-operators/

## Slide 40: Verilog Operators
Zero or not
All numbers except 0 are treated equally.

## Slide 41: Verilog Operators
If unsigned and signed wire signals are compared, signed signals will be treated as unsigned type.

## Slide 42: Verilog Operators
Bitwise operation
  Apply operator bit by bit
Concatenation, replication

## Slide 43: Verilog Operators
Shift operation
  Logical shift, arithmetic shift
Ternary conditional operation